## Slide 1: Alternative Portable Power Systems

## Slide 2: Amateur Radio Considerations
Radio communications during power outage
Remote operation
Extra points during contesting for use of alternative power source
Public service events

## Slide 3: System Key Components
Collect
  Solar, Wind, Hydroelectric, Human
Store
  Battery
Power
  AC, DC at the proper voltage and able to supply adequate current

## Slide 4
Collect
  Solar Panels from 7 to 90 watts
Store
  Battery packs from 8Wh, 2000mAh to 1200Wh, 100Ah
Power
  Capable of powering anything from a small LED light to Full-size Refrigerator

## Slide 5: Solar Panels

## Slide 6: Solar Panels Specs
Panel | Solar Capacity | Output | Weight
Nomad 7 | 7 watts | USB: 5V (up to 1.0A, regulated) Mini Solar: 6.5V (up to 1.1A un-regulated) Solar: 15V (up to 0.3A, regulated) | 0.8 lbs.
Nomad 13 | 13 watts | USB: 5V (up to 1.0A, regulated) Mini Solar: 6.5V (up to 1.1A un-regulated) Solar: 14-22V (up to 0.9A, un-regulated) | 1.6 lbs.
Nomad 20 | 20 watts | USB: 5V (up to 2.1A, regulated) Mini Solar: 6.5V (up to 1.1A regulated) Solar: 14-22V (up to 1.1A, un-regulated) | 2.5 lbs.
Boulder 15 | 15 watts | Solar: 14-16V (up to 1A, un-regulated) | 3.5 lbs.
Boulder 30 | 30 watts | Solar: 14-16V (up to 2A, un-regulated) | 6.5 lbs.
Boulder 90 | 90 watts | Solar: 14-22V (up to 6A, un-regulated) | 21.6 lbs.
Notes: Chainable
Monocrystalline Cells
Nomad 7 $80
Nomad 13 $160
Nomad 20 $200
Boulder 15
Boulder 30 $200
Boulder 90 $400

## Slide 7: Rechargers / Power Packs
Notes: Flip 10 $30
Switch 10 $40
Guide 10 $50

## Slide 8: Recharger Specs
Recharger | Capacity | Charge | Battery | Output | Weight
Flip 10 | 9.4Wh 3.6V 2600mAh | USB Up to 1A 5W max | Li-NMC | USB: 5V (up to 1.0A, regulated) | 2.5 oz
Switch 8 | 8Wh 3.7V 2200mAh | USB Up to 0.8A 4W max | Li-NMC | USB: 5V (up to 1.0A, regulated) | 3.2 oz
Switch 10 | 11Wh 3.7V 3000mAh | USB Up to 1A 5W max | 18650 By LG chem Samsung | USB: 5V (up to 1.5A, regulated) | 4.0 oz
Guide 10 | 11Wh 4.8V 2300mAh | Solar Up to 1.1A USB Up to 0.8A 4W max | Ni-MH | USB: 5V (up to 1.0A, regulated) | 4.6 oz
Notes: 18650 (aka 168A) 2200-3400mAh, 19 x 67 mm, larger that AA. This cell type is used in many laptop computer batteries
Ni-MH = Nickel–Metal Hydride Battery [Guide 10]
Li-NMC = Lithium Nickel Manganese Cobalt Oxide [Flip 10, Switch 8, Switch 10]

## Slide 9: Flip 10
Notes: $30
Charge Times
USB Power Source: 2.5 hours
Wall: n/a
Car: n/a
Nomad 7 Solar Panel: 2.5 - 5 Hours
Ports
USB Port (output): 5V, up to 1A (5W max), regulated
USB Port (input): 5V, up to 1A (5W max), regulated
Battery Details
Battery Type: Li-ion NMC
Battery Size: 9.4Wh (3.6V, 2600mAh)
Lifecycles: hundreds of cycles
Shelf-life: Keep plugged in, or charge every 3-6 months
Fuses: none
Management system: Charging and low-battery protection built-in
General
Chainable: No
Weight: 2.5 oz (70 g)
Dimensions: 3.6 x 0.75 x 0.75 in (9.2 x 1.9 x 1.9 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 12 months

## Slide 10: Switch 8
Notes: $40
Charge Times
USB Power Source: 4 hours
Wall: n/a
Car: n/a
Nomad 7 Solar Panel: 4-8 Hours
Nomad 13 Solar Panel: 4 Hours
Ports
USB Port (output): 5V, up to 1A (5W max), regulated
USB Port (input): 5V, up to 0.8A (4W max), regulated
Mini Solar Port (input): n/a
Battery Details
Battery Type: Li-NMC
Battery Size: 8Wh (3.7V, 2200mAh)
Lifecycles: hundreds of cycles
Shelf-life: Keep plugged in, or charge every 3-6 months
Fuses: none
Management system: Charging and low-battery protection built-in
General
Product SKU: 21004
Chainable: Yes
Weight: 0.2 lbs (91 g)
Dimensions: 1 x 1 x 5 in (2.5 x 2.5 x 12.7 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 6 months

## Slide 11: Guide 10
Notes: $50
$120 Guide 10 & Nomad 7
AA or AAA Batteries
Management system Charging and low-battery protection built-in
Charge Times
USB Power Source: 6-10 hours
Wall: n/a
Car: n/a
Nomad 7 Solar Panel: 3-6 Hours
Nomad 13 Solar Panel: 2.5-5 Hours
Ports
USB Port (output): 5V, up to 1A (5W max), regulated
USB Port (input): 5V, up to 0.8A (4W max), regulated
Mini solar port (input): 6.5V, up to 1.1A
Battery Details
Battery Type: NiMH
Battery Size: 11Wh (4.8V, 2300mAh)
Lifecycles: 500 cycles
Shelf-life: Keep plugged in, or charge every 3-6 months
Fuses: none
General
Product SKU: 21005
Chainable: No
Weight (w/batteries): 6.4 oz (181 g)
Dimensions: 2.5 x 4 x 0.75 in (6.4 x 10.2 x 1.9 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 6 months
User Guide: Download Here
Light Detail
LED Output: 100mW, white LED

## Slide 12: Power Packs
Notes: Sherpa 50 $230
Sherpa 100 $350

## Slide 13: Power Pack Specs
Power Pack | Capacity | Charge | Battery | Output | Weight
Sherpa 50 | 58Wh 11V 5200mAh | Solar 12V AC 14-25V Up to 2A 30W max | Li-NMC | USB: 5V (up to 1.5A, regulated) 6mm: 12V (up to 6A regulated) 9mm: 9-13V (up to 10A un-regulated, side) Laptop: 19V (up to 5A, regulated) AC Inverter: 110VAC (75W max, regulated) | 1.2 lbs.
Sherpa 100 | 98Wh 11V 8800mAh | Solar 12V AC 14-22V Up to 3A 45W max | Li-NMC | USB: 5V (up to 2.1A, regulated) 6mm: 12V (up to 10A regulated) 9mm: 9-13V (up to 10A un-regulated, side) Laptop: 19V (up to 6A, regulated) AC Inverter: 110VAC (100W max, regulated) | 1.9 lbs.
Notes: Li-NMC = Lithium Nickel Manganese Cobalt Oxide
Both Units have user replacable fuse

## Slide 14: Sherpa 50
Notes: **** Management system: Charging and low-battery protection built-in ****
$200 Sherpa 50
$410 Sherpa 50, Nomad 13 & Inverter
Charge Times
Wall Charger (30W): 3 hours
Car Charger (30W): 3 hours
Nomad 13 Solar Panel: 8-16 Hours
Nomad 20 Solar Panel: 6-12 Hours
Battery Details
Cell Type: Li-NMC
Peak Capacity: 58Wh (11V, 5200mAh)
Lifecycles: hundreds of cycles
Shelf-life: Keep plugged in, or charge every 3-6 months
Fuses: 15A, user replaceable fuse
Light
LED (output): 100mW, white LED
Ports
USB port (output): 5V, up to 1.5A (7.5W max), regulated
6mm port (output, 6mm, green, hexagon): 12V, up to 8A (100W max), regulated
laptop port (output, 7.4mm, orange, square): 19V, up to 5A (100W max), regulated
sidecar port (chain, 9mm): 9-13V, up to 10A (100W max)
AC inverter US (output, sold separately): 110V, up to 0.7A (75W max), 60Hz, modified sine wave
AC inverter Int. (output, sold separately): 220V, up to 0.35A (75W max), 50Hz, modified sine wave
charging port (input, 8mm, blue circle): 14-25V, up to 2A (30W max)
General
Product SKU: 11004
Chainable: Yes
Weight: 1.2 lbs (544 g)
UV Coated to prevent scratching
Dimensions: 4.5 x 1.5 x 5.25 in (11.4 x 3.8 x 13.3 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 6 months

## Slide 15: Sherpa 100
Notes: **** Management system: Charging and low-battery protection built-in ****
$350
$600 Sherpa 100, Nomad 20, AC Inverter
Charge Times
Wall Charger (45W): 3 hours
Car Charger (30W): 4 hours
Nomad 13 Solar Panel: 15-30 Hours
Nomad 20 Solar Panel: 10-20 Hours
Battery Details
Cell Type: Li-NMC
Pack Capacity: 98Wh (11V, 8,800mAh)
Single Cell Equivalent Capacity: 26,400mAh @3.7V
Lifecycles: hundreds of cycles
Shelf-life: Keep plugged in, or charge every 3-6 months
Fuses: 20A, user replaceable fuse
Light
LED (output): 100mW, white LED
Ports
USB port (output): 5V, up to 2.1A (10W max), regulated
6mm port (output, 6mm, green, hexagon): 12V, up to 10A (120W max), regulated
laptop port (output, 7.4mm, orange, square): 19V, up to 6A (120W max), regulated
sidecar port (chain, 9mm): 9-13V, up to 10A (120W max)
AC inverter US (output, sold separately): 110V, up to 0.9 (100W max), 60Hz, modified sine wave
AC inverter Int. (output, sold separately): 220V, up to 0.45A (100W max), 50Hz, modified sine wave
charging port (input, 8mm, blue circle): 14-22V, up to 3A (45W max)
General
Product SKU: 22002
Chainable: Yes
Weight: 1.9 lbs (864 g)
UV Coated to prevent scratches
Dimensions: 5.8 x 1.5 x 5.25 in (14.7 x 3.8 x 13.3 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 6 months

## Slide 16: Solar Generators
Notes: Yeti 150 $230
Yeti 400 $460
Yeti 1250 $1600

## Slide 17: Solar Generator Specs
Generator | Capacity | Charge | Battery | Output | Weight
Yeti 150 | 168Wh 12V 14Ah | Solar 12V AC 14-29V Up to 5A 60W max | AGM Lead-Acid | USB: 5V (up to 2.1A, regulated) 6mm: 12V (up to 10A regulated) Car Port: 12V (up to 10A regulated) AC Inverter: 110VAC (80W max, regulated) | 12 lbs.
Yeti 400 | 396Wh 12V 33Ah | Solar 12V AC 14-29V Up to 10A 120W max | AGM Lead-Acid | USB: 5V (up to 2.1A, regulated) 6mm: 12V (up to 10A regulated) Car Port: 12V (up to 10A regulated) AC Inverter 110VAC (80W max, regulated) Power Pole Chaining: 12V (up to 33A) | 29 lbs.
Yeti 1250 | 1200Wh 12V 100Ah | Solar 12V AC 16-48V Up to 10A 160W max | AGM Lead-Acid | USB: 5V (up to 2.1A, regulated) 6mm: 12V (up to 10A regulated) Car Port: 12V (up to 10A regulated) AC Inverter 110VAC (80W max, regulated) Power Pole: 12-14V (up to 30A) Power Pole Chaining: 12V (up to 175A) | 
Notes: Yeti 1250 Fuses: 200A (4x 50A fuses in parallel)

## Slide 18: Yeti 150
Notes: **** Management system: Charging and low-battery protection built-in ****
$230
$430 Goal Zero Yeti 150 & Nomad 20
Charge Times
Wall Charger (45W): 6 hours
Car Charger (30W): 8 hours
Nomad 13 Solar Panel: 26-52 Hours
Nomad 20 Solar Panel: 17-34 Hours
Boulder 15 Solar Panel: 22-44 Hours
Battery Details
Cell Type: AGM Lead-Acid
Peak Capacity: 168Wh (12V, 14Ah)
Lifecycles: hundreds of cycles
Shelf-life: Keep plugged in, or charge every 3-6 months
Fuses: 20A, user replaceable fuse
Ports
USB port (output): 5V, up to 2.1A (10W max), regulated
6mm port (output, 6mm, green, hexagon): 12V, up to 10A (120W max), regulated
12V car port (output): 12V, up to 10A (120W max)
AC inverter US (output, 60Hz, modified sine wave): 110V, 0.7A (80W continuous, 160W surge max)
charging port (input, 8mm, blue, circle):14-29V, up to 5A (60W max)
General
Product SKU: 22004
Chainable: No
Weight: 12 lbs (5.4 kg)
Dimensions: 7.75 x 5.75 x 6.75 in (19.7 x 14.6 x 17.2 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 6 months

## Slide 19: Yeti 400
Notes: **** Management system: Charging and low-battery protection built-in ****
$460
$660 Yeti 400 & Nomad 20
Charge Times
Wall Charger (72W): 5 hours
Car Charger (30W): 13 hours
Boulder 30 Solar Panel: 26-52 Hours
Battery Details
Cell Type: AGM Lead-Acid
Peak Capacity: 396Wh (12V, 33Ah)
Lifecycles: hundreds of cycles
Shelf-life: Keep plugged in, or charge every 3-6 months
Fuses: none
Ports
USB port (output): 5V, up to 2.1A (10W max), regulated
6mm port (output, 6mm, green, hexagon): 12V, up to 10A (120W max)
12V car port (output): 12V, up to 10A (120W max)
AC inverter US (output, 60Hz, pure sine wave): 110V, 2.6A (300W continuous, 600W surge max)
Power Pole Chaining port: 12V, up to 33A (400W max)
charging port (input, 8mm, blue, circle):14-29V, up to 10A (120W max)
General
Product SKU: 23000
Chainable: Yes
Weight: 29 lbs (13.2 kg)
Dimensions: 10.25 x 8 x 8 in (26 x 20.3 x 20.3 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 6 months

## Slide 20: Yeti 1250
Notes: ***** Management system: MPPT charge controller, low battery protection ******
$1400
$1800 Yeti 1250, 2 x Boulder 30, Roll Cart, Solar Panel Travel Case
Charge Times
Wall Charger (72W): 18 hours
Car Charger (30W): 44 Hours
2 x Boulder 30: 40-80 Hours
3 x Boulder 30: 27-54 Hours
Battery Details
Cell Type: AGM Lead Acid
Peak Capacity: 1200Wh (12V, 100Ah)
Lifecycles: hundreds of cycles
Shelf-life: Keep plugged in, or charge every 3 months
Fuses: 200A (4x 50A fuses in parallel)
Ports
USB port (output): 5V, up to 2.1A (10.5 W max), regulated
6mm port (output, 6mm): 12V, up to 10A (120W max)
12V car port (output): 12V, up to 10A (120W max)
12V Power Pole Port (output): 12-14V, up to 30A (360W max)
AC inverter (output, pure sine wave): 110V 10A (1200W continuous, 1500W surge max)
Charging port (input, 8mm): 16-48V, up to 10A (160W max)
Power Pole charging port (input): 16-48V, up to 20A (240W max)
Power Pole chaining port: 12V, up to 175A (2100W max)
General
Product SKU: 31901
Chainable: Yes
Weight: 103 lbs (46.7 kg)
Dimensions: 11 x 16 x 14.5 in (27.9 x 40.6 x 36.8 cm)
Operating usage temp.: 32-104 F (0-40 C)
Certs: CE, FCC, ROHS
Warranty 6 months

## Slide 21: Charge Times
Charge Time in Hours | Nomad 7 | Nomad 13 | Nomad 20 | Boulder 15 | Boulder 30 | Boulder 90
Switch 8 | 4-8 | 4 | 4 | Not Compatible | Not Compatible | Not Compatible
Switch 10 | 4-8 | 4 | 4 | Not Compatible | Not Compatible | Not Compatible
Guide 10 | 3-6 | 2.5-5 | 2.5-5 | Not Compatible | Not Compatible | Not Compatible
Sherpa 50 | Not Recommended | 8-16 | 6-12 | 8-16 | 4-8 | 1-3
Sherpa 100 | Not Recommended | 15-30 | 10-20 | 13-26 | 7-14 | 3-6
Yeti 150 | Not Recommended | 26-52 | 17-34 | 22-44 | 11-22 | 3-6
Yeti 400 | Not Recommended | Not Recommended | 40-80 | 53-106 | 26-52 | 9-18
Yeti 1250 | Not Recommended | Not Recommended | Not Recommended | Not Recommended | 80-160 | 27-54

## Slide 22: Charge Your Device
Charge Times | Headlamp 4Wh | Smartphone 5-6Wh | GoPro 5Wh | Digital Camera 8Wh | Tablet 25-42Wh | Laptop 50Wh
Switch 8 | 2 | 1 | 1-2 | 1 | 25% Boost | N/A
Switch 10 | 2 | 1 | 1-2 | 1 | 25% Boost | N/A
Guide 10 | 2 | 1 | 1-2 | 1 | 1-2 | 1
Sherpa 50 | 12 | 7 | 9 | 5 | 1-2 | 1
Sherpa 100 | 25 | 14 | 18 | 10 | 2-4 | 1-2
Yeti 150 | 37 | 15 | 25 | 12 | 6 | 1-2
Yeti 400 | 100 | 30+ | 70+ | 20+ | 10+ | 3-5
Yeti 1250 | 300+ | 100+ | 200+ | 100+ | 45+ | 20+

## Slide 23: Lights
Notes: Lighthouse 250 $80
Torch 250 $80

## Slide 24: Light Specs
Light | Capacity | Charge | Battery | Output | Weight
Lighthouse 250 | 16.3Wh 3.7V 4400mAh | USB Up to 1A 5W max | Li-NMC | Light: 250 Lumens USB: 5V (up to 1.5A, regulated) | 1.1 lbs.
Torch 250 | 16.3Wh 3.7V 4400mAh | Solar 0.8W USB Up to 1A 5W max | Li-NMC | Light: 250 Lumens USB: 5V (up to 1.5A, regulated) | 14.4 oz

## Slide 25: Lighthouse 250
Notes: $80
Run Times
One side lit: 48 hours (low), 12 hours (high), 5 hours (turbo)
Both sides lit: 24 hours (low), 6 hours (high), 2.5 hours (turbo)
Hand Crank: 2.2W (cranking at 120 RPM), 1 minute of crank = 10 minutes of light
Light
LED (output): 2x3W, warm white CREE LED, 250 Lumens
Battery:
Cell Type: Li-NMC
Cell Capacity: 16.3 Wh (3.7V, 4400mAh)
Lifecycles: hundreds of cycles
Shelf Life: Keep plugged in, or charge every 3-6 months
Management System: Charging and low-battery protection built-in
Ports
USB port (output): 5V, up to 1.5A (7.5W max), regulated
USB port (input): 5V, up to 1A (5W max
General
Product SKU: 32001
Chainable: No
Weight: 1.1 lbs (498 g)
Dimensions: 4.5 x 5 x 6.6 in (11.5 x 12.7 x 16.5 cm)
Certs: CE, FCC, ROHS
Warranty 12 months

## Slide 26: Torch 250
Notes: $80
Charge Times
Goal Zero Nomad 7: 7-14 hours
Built in Solar: 23-46 hours
USB Source: 7 Hours
Run Times
Spot Light: 15 hours (low), 7 hours (high)
Flood Light: 48 hours (low), 22 hours (high)
Hand Crank: 2.2W (cranking at 120 RPM), 1 minute of crank = 2 minutes of light
Light
LED (output): 250 Lumens, 4000K warm white cree LED's
Spot Light: 180 Lumens
Flood Light: 70 Lumens
Solar
Rated Power: 0.8W
Cell Type: Monocrystalline
Battery
Cell Type: Li-NMC
Cell Capacity: 16.3 Wh (3.7V, 4400mAh)
Lifecycles: hundreds of cycles
Shelf Life: Keep plugged in, or charge every 3-6 months
Management System: Charging and low-battery protection built-in
Ports
USB port (output): 5V, up to 1.5A (7.5W max), regulated
USB port (input): 5V, up to 1A (5W max)
General
Chainable: No
Weight: 14.4 oz (408 g)
Dimensions: 10 x 3.5 x 1.75 in (25.4 x 8.9 x 4.5 cm)
Operating Useage Temp: 32-104 F (0-40 C)
Warranty 6 months

## Slide 27: Ham Decision
Buy a Manufactured Kit
  Sherpa 50 = $410
  Sherpa 100 = $600
  Yeti 150 = $430
  Yeti 400 = $660
  Yeti 1250 = $1800
Build Your Own

## Slide 28: What Your Build Should Include
Solar Panel
Charge Controller
Batteries
Low Battery Protection
Output Regulator
Connectors
Wire
Housing
Plan that all the components work together

## Slide 29: Build Plan
Budget
Equipment System will power
Capacity of System
  Storage
  Max Output
Size of System (Physical & Weight)